## Slide 1: Declination
Using the earth’s magnetic field to find direction

## Slide 2: Declination
What is declination?
  Declination is the angle between magnetic north and true north.
Why does it matter?
  Because compasses align with magnetic north and maps align with true north.

## Slide 3: Declination
What else is important?
Declination is complex
Declination changes with time
What if you don’t have an adjustable compass?
You have to add or subtract the adjustment
Based on east or west declination
Based on compass to map, or map to compass

## Slide 4: World Declination: 2018

## Slide 5: Declination: Western US 2018

## Slide 6: Current Declination: Community Center
15.62° E, changing by 0.1° W per year
http://www.ngdc.noaa.gov/geomag-web/#declination
Or search for “magnetic declination”

## Slide 7: How do You Correct for Declination?
Do the math
Mnemonics
“Set it and forget it.”

## Slide 8: Do the Math: Correcting a Magnetic Bearing for East Declination
TB
TN
MB

Pt. B
TB =  + MB

## Slide 9: Mnemonics:
Declination East, Compass Least
Empty Sea add Water
Declination West, compass best
True to Mag, Subtract East
Mag to True, add East

## Slide 10: “Set it and Forget It” How to Set Declination
Use screw driver to twist adjustment screw.
Set to 16° E. Use the line in the middle of the south end of the orienting arrow.
The orienting arrow should point east of north.

## Slide 11: Questions?

## Slide 12: Break Time

## Slide 13: Compass use
How to enhance your sense of direction with a tool

## Slide 14: Compass

## Slide 15: Compass: Parts and Use
Sighting mirror
Base plate
Rotating bezel with azimuth ring
Direction of travel arrow
Orienting lines
Needle with box

## Slide 16: Compass: Bearing to an Object
Point the direction arrow toward the object, holding the compass level, and sighting along the sight lines.
Twist the dial until the magnetic needle lines up with the orienting arrow.
Read the bearing in degrees by looking at the tick on the dial at the direction pointer.

## Slide 17: Compass: Bearing onto a Map
With your compass set to the bearing you took – use 185° – put it on the map.
Line up one of the straightedges with your position or a known landmark. Use Paradise Visitors Center.
Turn the baseplate, keeping the straightedge on your point, until the north on the graduated dial points to the map’s true north.
Follow the straightedge to the destination.
Notes: Denman Peak is the destination or target.

## Slide 18: Compass: Bearing onto a Map
Notes: Should be Denman Peak

## Slide 19: Compass: Bearing from a Map
Put your compass on the map, lining up a straightedge so that both your starting point and the destination lie along it. Use Paradise Visitors Center and Sluiskin Falls.
Twist the graduated dial, keeping the straightedge on both points, until the north on the graduated dial points to the map’s true north.
Read the bearing in degrees by looking at the tick on the dial at the direction pointer.

## Slide 20: Compass: Bearing from a Map
Notes: Should be 60°

## Slide 21: Compass: Triangulation
Triangulation is using the intersection of two lines to find your location.
What kinds of lines on might work?
  Ridges, valleys, and creeks
  Contour lines, if you know your elevation
  Trails, roads, power lines, etc.
  One or more compass bearings

## Slide 22: Compass: Triangulation Exercise
Notes: Use 325° to west shore of Reflection Lakes and 12° to the east shore of Louise Lake.

## Slide 23: Compass: More Triangulation

## Slide 24: Compass: Orient a Map
      Set the graduated dial so that north lines up with the direction pointer.
      Line up one of the compass’s straightedges so that it’s lined up with a north-south line on the map.
      Keeping the map and compass pressed together, so they don’t shift relative to each other, turn the map until the compass needle is lined up in the orientation arrow.

## Slide 25: Compass: Follow a Bearing
Distance using time
Time yourself to a point with known distance
Keep track along the way
Distance using your pace
Step is 30 – 35”
Pace is two steps, around 5’
Speed and incline affect pace length

## Slide 26: Compass: Follow a Bearing
Procedures
Sight on a nearby object and walk to it.
Sight on a partner and walk to him or her.
Use back-bearings.
Communicate
Repeat.

## Slide 27: Plug for our Library

## Slide 28: Extra Slides

## Slide 29: Declination: World

## Slide 30: Declination: US 2015

## Slide 31: Declination: Washington 2010